# NetPlug – pluggable automation network
Thought to, but not limited to control arduino microcontrollers over lan or wan using openHAB or using other ways.
## supported device types
- statefull actors
  - R – relais (state: 0/1, on/off)
  - D – digitaler pwm output (state: 0-255)
- stateless actors
  - S – remote controll (sends a number)
  - P – relais used as a push button (activates the relais for a short time span)
- sensors
  - A – analog input
  - T – temperature sensor (state: temperature*100, e.g. (sensor having ID=3 detects 21,12°C): ST3= 2112
  - I – remote controll (receives a number)
## version history and outlook
- 2013/2014 – NetPlugV1
  - working implementation of
    - udp based lan communication (broadcast, direct control)
    - http based wan communication (using a simple router php script, push and pull at both ends)
  - supported devices
    - arduino network adapters
      - w5100
        - udp
        - http
      - enc	28j60
        - udp
- comming soon – NetPlugV2
  - authentication based on signatures
  - other communication ways beside lan
    - bluetooth
    - usb
    - over the air – however
## protocol – NetPlugV1
All messages are encapsulated as follows:
NetPlugV1|message
### Broadcast (B=Broadcast)
The microcontrollers, the netplug shares it's state:
NetPlugV1|B:R0=0,R1=1
The first relais is switched off (0), the second one is on (1).
### Controll (S=Set)
The first relais (ID=0) gets switched on:
NetPlugV1|S:SR0=1
### Response (M=Message)
Using http as transport, there is an easy way to respond to controll messages or pull requests (that are empty somehow).
NetPlugV1|M:OK
or
NetPlugV1|M:Error, illegal ...
## Configuration of openHAB items
- lan via UDP:
  - netplug=udp://IP:Port/TypeId
### example
Group NetworkPlug	"network-plug" <corridor> (test)
Switch NetworkPlug0	"plug 0" (NetworkPlug) { netplug="192.168.178.40:R0" }